FISHER ARMSTRONG PLANNING DISTRICT

RM of Armstrong        Box 69, Inwood, MB R0C 1P0 		  204-278-3377	         cao@rmofarmstrong.com

RM of Fisher	  Box 280 Fisher Branch, MB R0C 0Z0	  204-372-6393           rmoffisher@mts.net

BUILDING INSPECTOR

DAVE METNER

Ph.: 204-302-0890;  email: davebuildinginspector@yahoo.com

THE CONTRACTOR AND OWNER ARE EQUALLY RESPONSIBLE TO

CALL FOR THE NECESSARY INSPECTIONS

24 HOUR NOTICE FOR INSPECTIONS IS REQUIRED

PERMIT CARD MUST BE POSTED AT SITE – FAILURE TO DO SO WILL RESULT IN A FINE

INSPECTION SCHEDULE:

- FOOTING / PILES / PIERS / THICKEND EDGE SLABS

Forms, granular material, poly & reinforced steel tied and supported - ready for concrete.

- BASEMENT WALLS / GRADE BEAMS

Forms with reinforced steel in place and tied - ready for concrete.

- BACKFILLING

Concrete Basement - damp proofing, drain pipe or tile in place and covered with course granular drainage material.

Wood Basement - Framing, caulking, moisture barrier (6 mil 656B poly) cover plate, poly protection and granular drainage layer in place (backfill material to have good drainage ability).

Crawl Space – Drain tile and sump, frost protection.

- ATTACHED GARAGE (if applicable)

Piers, grade beam and slab.

- FRAMING AND PLUMBING

Framing - Have truss and engineered floor information on site for inspection.

Plumbing - Drain waste vent rough in.  Plumbing drain waste lines under slabs to be left open for inspection to sewer connection.

- INSULATION AND VAPOUR BARRIER

Insulation - fill entire cavity, all plumbing and wiring penetrations (through interior top plates to attic) to be sealed.

Vapour Barrier - installed and sealed as per Manitoba Building Code.

- FINAL INSPECTION (MECHANICAL)

Includes heating, ventilation, plumbing, crawl space and basement (joist header insulation etc.)

Note:    For each re-inspection made after the owner/applicant/contractor has been notified

of defects and where, upon re-inspection, it is found that the defects have not been remedied, a penalty fee of $50.00 plus mileage will be charged.

____________________________________________________________________________

PLEASE CONTACT BUILDING INSPECTOR FOR INSPECTIONS AT THE APPROPRIATE LEVELS OF CONSTRUCTION

If necessary please leave a message, include your name, contact phone number, permit number, address of inspection site, date and time inspection is required.